## Slide 1
Managing life-cycle information:
from IGN France’s BDUni to the OME2 project
Noémie Grémeaux (IGN-France)

## Slide 2: Contents
IGN France’s BDUni
The BDUni management system
Use and re-use of the BDUni management system

## Slide 3: 1. IGN France’s BDUni
Pointe à Colombier, Saint-Barthélemy – IGN

## Slide 4: IGN France’s BDUni
IGN France’s BDUni
IGN France’s central production database
Created in 2006
1:10k multi-theme vector data
  Buildings
  Administrative
  Hydrography
  Land cover
  Named places
  Transport
  …
200 tables and 1800 fields
~180 million live objects and 450 million historical objects
690 Go
PostgreSQL/PostGIS
EBM
ERM
BDUni
Database products
Paper maps
Pan-European products
Web services

## Slide 5: Updating the BDUni
IGN France’s BDUni
IGNF Central management team
IGNF field agent
Collaborative tools
External partner
BDUni

## Slide 6: The BDUni management system
Workflow
 Many users are working on the BDUni at the same time so conflicts can occur.
 It is essential to track changes and know who has been doing what.
Main purposes of the BDUni management system:
Keep track of all changes performed on the data through the different tools.
Record every version of every object in the database, in order to visualize evolutions and provide incremental updates.
Manage updates from the different tools and handle conflicts.
IGN France’s BDUni
BDUni
Extract data from server
Modify data locally
Push updates on server

## Slide 7: 2. The BDUni management system
Grand récif du nord-est, Mayotte – IGN

## Slide 8: Implementation
7 technical fields on all tables
A history table for each table
To store all the successive versions of every object
PostgreSQL triggers
To fill the required information in case of modifications:
UID updating rules (cleabs)
Technical fields (dates, destroyed…)
History tables.
destroyed true/false
unique identifier
dates
to handle conflicts
The BDUni management system

## Slide 9: History table example
The BDUni management system
Main table
History table
Current version of the object
Former versions of the object

## Slide 10: Management rules
 | Main table | History table
Object created | New entry Fill creation date Generate fingerprint | -
Object modified | Fill modification date Update fingerprint | Record former version
Object deleted | Set « destroyed » field to true Fille deletion date Update fingerprint | Record former version
The BDUni management system

## Slide 11: Handling conflicts
The BDUni management system
A user extracts some BDUni data and modifies an object  the object is modified only locally for now
The modified object is sent to the BDUni server with all its attributes, including its original gcms_fingerprint
Does gcms_fingerprint have the same value on the modified object as on the server version of the object ?
The object is recorded on the server and the technical fields/history tables ares filled according to the management rules
The object is rejected. Help is provided to the users to solve the conflict through a dedicated interface.
Once he has solved the conflict, the user can try to send his modification again
It means that another user has modified the object between the time when the data was extracted and the time when the modified object was sent.
Yes
No

## Slide 12: 3. Use and re-use of the BDUni management system
Pointe à Colombier, Saint-Barthélemy – IGN

## Slide 13: Accessing historical information
On the « Collaborative space » website* (https://espacecollaboratif.ign.fr)
Ex: https://espacecollaboratif.ign.fr/gcms/database/bdtopo_metropole/feature-type/troncon_de_route/feature/TRONROUT0000000013612462/versions
* For registered users only
Use and re-use of the BDUni management system

## Slide 14: Delivering incremental updates
A change-only updates edition of the BDUni is available every trimester.
On the « Collaborative space » website, registered users can download change-only updates on request.
Use and re-use of the BDUni management system

## Slide 15: Setting up databases with life-cycle management for our partners
Two simple parameters on the Collaborative space
Automatic creation of technical fields and triggers
Use and re-use of the BDUni management system

## Slide 16: Open Maps for Europe 2
Consortium led by EuroGeographics
  IGN France
  Kadaster Netherlands
  NGI Belgium
  Hellenic Cadastre
  Spanish Cadastre
Co-funded by the European Commission
To create a production process for:
  An open large-scale database
  Containing key themes: Administrative units, Transport network, Hydrography
  With authoritative, harmonised and edge-matched data
  Including life-cycle management (INSPIRE compliant).
Use and re-use of the BDUni management system
Central OME2 database
Life-cycle management
Model conversion
Edge-matching
1:10k-1:25k
  IDOX
  BKG

## Slide 17: Capitalizing on the BDUni experience
Similar concepts: unique identifier and life-cycle attributes
The same principles are being implemented in the OME2 database:
  History tables
  Re-use of the BDUni triggers to fill the life-cycle information.
 A functional life-cycle management system with very little additional implementation.
Use and re-use of the BDUni management system
BDUni
OME2

## Slide 18
Thank you for your attention
Contact: noemie.gremeaux@ign.fr

## Slide 19: Réduire / Augmenter le niveau de liste
1 & 2
Pour augmenter le niveau de liste :
    (Ex. : pour passer du texte de niveau 1 au texte de niveau 2 sur la page suivante)
    Sélectionner le texte de niveau 1 sur la page de texte
    Menu Accueil / Augmenter le niveau de liste (2)
    Cette opération permet de passer au niveau de texte suivant
Pour réduire le niveau de liste :
    (Ex. : pour passer du texte niveau 2 au texte niveau 1 sur la page suivante)
    Sélectionner le texte niveau 2 sur la page de texte
    Menu Accueil / Réduire le niveau de liste (1)
    Cette opération permet de passer au niveau de texte précédent
Méthodologie

## Slide 20: Titre
Texte de niveau 1
  Texte de niveau 2
    Texte de niveau 3
      Texte de niveau 4
        Texte de niveau 5
Titre de partie
  Sous-titre de partie

## Slide 21: Couleurs
La palette de couleurs à utiliser est celle présente dans ce modèle.
Titre de partie
  Sous-titre de partie

## Slide 22: Copier / coller les textes
À partir d’une ancienne présentation
    Sélectionner et copier les textes de votre ancienne présentation
    Sélectionner la zone texte de la nouvelle présentation
    Cliquer sur « Accueil / Coller (sélectionner la petite flèche sous l’icône Coller) / Collage spécial »
    Cocher « Coller », « Texte sans mise en forme » et « OK »
    Il faut ensuite appliquer les niveaux de texte à l’aide des outils « Réduire / Augmenter le niveau de liste »
Méthodologie

## Slide 23: Modifier les logotypes partenaires
Modifier les logotypes partenaires dans les masques :
    Menu « affichage » / « Masque des diapositives »
    Les remplacements de logotypes se fera sur les trois premiers masques
      Masque 1 correspond aux pages 3, 4, 5 et 6
      Masque 2 correspond à la page de couverture 1
      Masque 3 correspond à la page de titre 2
    Sélectionner l’image d’emplacement du logotype partenaire
    Menu « Format » / « Remplacer l’image »
    Choisissez l’image de votre choix
    Cliquer sur « Insérer »
    Menu « Affichage » / « Normal »
Méthodologie